## Slide 1: Towards BIM with underground point clouds and geomodels
106th OGC Technical Committee, GeoScienceDWG session
Orléans, France
Thomas Dewez, Dept. Risks & Mitigation, BRGM
22 March 2018

## Slide 2: Take home message
BIM requires knowledge of underground properties
BRGM is gathering momentum to meet the expectation
  Use a generic API allowing to query geological model at any location and allowing to join point clouds and geomodels
  Scalable approach to any BIM object, not just underground cavities

## Slide 3: Context and opportunities
Geological urban models are a growing demand for urban development planning
Traditional borehole data are not ubiquitous
Cavities offer a unexploited glimpse of the geology
Orleans has >700 underground cavities on its territory
  Many are former building stone quarries
  Some are karstic caves
Cavity collapse is a high local hazard
Outside of surface observations and boreholes, geomodelling tools do not know what to do with 3D cavities

## Slide 4: Underground mapping technology
Handheld laser scanner : What can a Zeb do for us?
GeoSLAM Zeb-Revo

## Slide 5: La Bordé quarry Orleans case study
Movie
Quarry between -9 and -14m below the ground
Roof collapse
Ventilation shafts
Access staircase

## Slide 6: Survey characteristics
  Product types:
    Location maps of the cavity with respect to cadastre and surface assets
    Thickness of overburden, floor to ceiling height (collapse susceptibility parameters)
    Existing disorder (vault collapse, rubble piles)
    Fragility features (bedding, fractures, …)
Overburden thickness
Gallery height
Floor topography

## Slide 7: From point cloud to ground properties
To infer rock properties behind gallery walls > Geomodelling
Geomodelling tools expect sparse and discrete information
  Based on geologist’s field note book, boreholes, geophysics
  Typically less than 10’000 observation points with weak precision
Geological models do not expect voids
Creating interactions between ~100Mpts in 3D and geomodels is a challenge

## Slide 8: Interactions between model and point clouds
Geomodels natively are represented & discretized by meshed grid (tetrahedra)
  Point clouds needs meshing (not trivial – requires normals)
  Meshing is solved at point cloud processing end
2 levels of interaction between 3D galleries and geomodel
  Label gallery wall triangles with geological formation they lie in. Visualisation to confirm modelling hypothesis
  Constrain geomodel with structural data extracted from the gallery point cloud geometry

## Slide 9: Level 1: Query model with gallery points
3D geomodel is created from scratch over the domain
  3 horizontal layers at realistic depths
At point cloud end
  Decimate point cloud
  Mesh it for visu & carving holes into model
At geomodelling end
  Generic SCUDDD API queries 2 predicates :
  In which layer is this point?
   Does an interface split this triangle?
The SCUDDD generic query API is fully applicable to BIM points and faces

## Slide 10: Level 2: Refine geomodel with cavity geometry
At point cloud end
  Structural mapping tools (FACETS or COMPASS) are used to generate structural data objects as wkt (center XYZ, size, dip, strike)
At geomodelling end
  Structural data is imposed as geopotential constraints
Real la Bordé quarry structural data
Geomodel on a complexe geology
Structural data

## Slide 11: Implications for BIM
Geomodels can be turned into geotechnical models by adding rock properties on cells
Generic geomodel querry API concept readily applicable to foundation faces and vertices
Limit pressure pl* (metric for foundations)
Weathered: 0.5 – 1 Mpa
Upper facies: 1.5 – 2.5 Mpa
Calcaire de Beauce: 4 Mpa

## Slide 12: Aknowledgements
This work is a BRGM team effort bringing together experts in mapping, geotechnics, geomodelling, and local authorities
Geomodelling team
  Cécile Allanic, Gabriel Courrioux, Simon Lopez
3D mapping team
  Silvain Yart, Florian Masson, Thomas Dewez
Geotechnics
  Gildas Noury
SCUDDD API
  Christelle Loiselet, Christian Bellier, Simon Lopez, Gabriel Courioux
Local authorities (Orléans metropole)
  Imed Ksibi