## Slide 1: Standardizing geomodeling and geotechnical data exchanges: the SCUDDD and MINND projects
104th OGC Technical Committee – GeoScience DWG session
Southampton, United Kingdom
Mickaël BEAUFILS
14 September 2017

## Slide 2: Standardizing geomodelling exchange
Statement
  Several geomodelling tools exist (e.g. two « homemade » tools exist in BRGM) and have their own native format,
  Geomodels shall be updated by considering new available data,
  Conversion between format is often tricky and not lossless
Rationale
  Having a pivot format would probably mean maintaining at least two formats:
    The raw data format,
    The “to share” format
Is there other solutions?

## Slide 3: How to cope with users thirst of geological models data?
Expression of the “geological architecture” (P. Calcagno & al.)
  “How geology is here”
    Define which geological units are involved
    Define relationship between them (onlap, erod, …)
  Not about geometries expression and exchange
Develop APIs to query geological models stored in their native formats (SCUDDD project: C. Loiselet & al.)
  Extraction of relevant code from the geomodelling tools to query the model
  Develop services to build on demand representations and visualizations

## Slide 4: SCUDDD architecture
WPS
SCUDDD methods
Interface
Delivery
SCUDDD_API
Native directory of geomodels
Model part
iSCUDDD_GEOL = Model queries / responses :
1) which formation?
2) which contact?
- Geologic logs
- Profiles
- Maps
- Points cloud
- TIN
- 2D/3D regular grid
- 2D/3D irregular grid
- ….
Representations
(machine readable)
Visualizations
(human readable only)
(adapted from Loiselet & al., 2016)

## Slide 5: SCUDDD interface

## Slide 6: The MINND project
http://www.minnd.fr/en/
Interoperable Information Model for Sustainable Infrastructures
A French consortium of 60 partners
1 goal: enhancing BIM capabilities for infrastructure modeling and management
In relationship with its environment

## Slide 7: Underground Infrastructure use case (UC8)
14 partners
2 working groups
  Developing / adjusting IFC standards to describe Underground Infrastructure and its equipment
  Describe relationship between built part and environment and standardize geotechnical data exchanges (Lead by BRGM)
5 main actions
  Cartography of data exchanges
  Elicitation of semantics
  Conceptual model definition
  Definition of data access and representations
  Standardization through BSI and OGC

## Slide 8: What do we have in MINND?
Targetting the « Holy Grail » BIM level 3
  BIM level 2 ~ Exchange data in standardized format (IFC)
  BIM level 3 ~ Service approach and data centralization
Revisiting some French normative documents (AFNOR, CETU) on which data shall be exchanged at which moment of the project + update & adjust with experience of the team
Feedback from first meetings:
  Geotechnical data are mostly geoscience data
  Geological models / geotechnical models are shaped and reshaped until uncertainty assessment is « acceptable »
  We can (shall?) use our classical tools to provide data (O&M, WFS, …) + maybe have to address (again?) the uncertainty assessment topic

## Slide 9: Opportunities about geomodelling standardization
Geology Architecture
  Might be a very good linked data use case ?
  Same features but with different relations depending on location
Standardizing geomodeling querying
  By defining standard requests + parameters
  By defining standardized outputs
  By developing more APIs linked to geomodelling tools in order to be able to handle more native formats

## Slide 10: Opportunities with geotechnical data standardization
Construction domain is a big geoscience data producer and consumer
  MINND UC8 offers a very applied use case to demonstrate usage of standardized geoscience data in production mode
  Facilitate data transfer from construction domain to geoscience community to enhance our capacity of understanding subsurface
  Facilitate data integration in modelling process while construction works are realised
Collaboration between BSI and OGC
  Positioning OGC standards as solutions to help reaching BIM level 3
  Perhaps not only for GeoScience data…(WFS to serve IFC?)