# Open Geospatial Consortium, Inc.

Date: 2011-07-01

Reference number of this document: OGC 11-xxxx

Version: 0.1.0

Category: OGC™ Interoperability Experiment Report

Editors: xx

# OGC® Surfacewater Interoperability Experiment

# FINAL REPORT

Copyright © 2010 Open Geospatial Consortium, Inc. All Rights Reserved.
To obtain additional rights of use, visit http://www.opengeospatial.org/legal/.

# Warning

This document is not an OGC Standard. This document presents a discussion of technology issues considered in an initiative of the OGC Interoperability Program. This document does not represent an official position of the OGC. It is subject to change without notice and may not be referred to as an OGC Standard. However, the discussions in this document could very well lead to the definition of an OGC Standard. Recipients of this document are invited to submit, with their comments, notification of any relevant patent rights of which they are aware and to provide supporting documentation.

Document type: 	OpenGIS® Engineering Report

Document subtype:	NA

Document stage: 	Not approved for public release

Document language: 	English

# Preface

This report describes the methods, results, issues and recommendations generated by the Surfacewater Interoperability Experiment (SW IE), carried out as an activity of the OGC Hydrology Domain Working Group (HDWG). The SW IE is designed to:

Suggested additions, changes, and comments on this draft report are welcome and encouraged. Such suggestions may be submitted by email message or by making suggested changes in an edited copy of this document.

The changes made in this document version, relative to the previous version, are tracked by Microsoft Word, and can be viewed if desired. If you choose to submit suggested changes by editing this document, please first accept all the current changes, and then make your suggested changes with change tracking on.

Contents	Page

1	Introduction	1

1.1	Scope	1

1.2	Document contributor contact points	2

1.3	Revision history	2

1.4	Future work	2

1.5	Forward	2

2	References	4

3	Terms and definitions	6

4	Conventions	7

4.1	Abbreviated terms	7

4.2	UML notation	8

5	SWIE Overview	9

5.1	Background	9

5.2	Motivation and Goals	9

5.3	User Scenarios	9

5.4	Use Cases	9

6	SWIE Architecture	10

6.1	Motivation and Goals	10

6.2	Design and Implementation	10

6.3	Architectural Issues and Recommendations	10

7	SWIE Best Practices AND outstanding issues	11

7.1	SWIE Services Profile	11

7.2	Issues and Recommendations	11

7.3	SWIE WaterML 2 Profile	12

8	SW IE Client Implementation	13

8.1	Motivation and Goals	13

8.2	Client	13

8.3	University of Calgary (UC)	13

8.4	34 North (34N)	13

9	Acknowledgements	14

Figures	Page

No table of figures entries found.
In your document, select the words to include in the table of contents, and then on the Home tab, under Styles, click a heading style. Repeat for each heading that you want to include, and then insert the table of contents in your document. To manually create a table of contents, on the Document Elements tab, under Table of Contents, point to a style and then click the down arrow button. Click one of the styles under Manual Table of Contents, and then type the entries manually.

# Introduction

## Scope

This report describes the methods, results, issues and recommendations generated by the Surfacewater Interoperability Experiment (SW IE), carried out as an activity of the OGC Hydrology Domain Working Group (HDWG). The SW IE is designed to:

The SW IE concluded

Attention is drawn to the possibility that some of the elements of this document may be the subject of patent rights. The Open Geospatial Consortium Inc. shall not be held responsible for identifying any or all such patent rights.

Recipients of this document are requested to submit, with their comments, notification of any relevant patent claims or other intellectual property rights of which they may be aware that might be infringed by any implementation of the standard set forth in this document, and to provide supporting documentation.

## Document contributor contact points

All questions regarding this document should be directed to the editors or contributors:

| Name | Organization |
| --- | --- |

## Revision history

| Date | Release | Editor | Primary clauses modified | Description |
| --- | --- | --- | --- | --- |

## Future work

Future improvements to this document are desirable to clarify technical details arising from subsequent implementation of OGC standards and related technologies.

Aspects of the SW IE will continue informally amongst participants interested in maintaining and expanding surfacewater data sharing.

## Forward

This is an information document that describes the methods, issues, solutions, and recommendations relevant to the SW IE.

Attention is drawn to the possibility that some of the elements of this document may be the subject of patent rights. The Open Geospatial Consortium Inc. shall not be held responsible for identifying any or all such patent rights.

Recipients of this document are requested to submit, with their comments, notification of any relevant patent claims or other intellectual property rights of which they may be aware that might be infringed by any implementation of the standard set forth in this document, and to provide supporting documentation.

# References

The following documents are referenced in this document. For dated references, subsequent amendments to, or revisions of, any of these publications do not apply. For undated references, the latest edition of the normative document referred to applies.

OGC 01-068r3, Web Map Service Implementation Specification, 1.1.1, 2002-01-16, http://www.opengeospatial.org/standards/wms

OGC 04-094, Web Feature Service Implementation Specification, 1.1.0, 2005-05-03, http://www.opengeospatial.org/standards/wfs.

OGC 04-095, OpenGIS Filter Encoding Implementation Specification, 1.1.0, 2005-05-03, http://portal.opengeospatial.org/files/?artifact_id=8340.In addition to this document, this report includes several XML Schema Document files as specified in Annex A.

OGC 06-009r6, OpenGIS Sensor Observation Service, 1.0, 2007-10-26, http://www.opengeospatial.org/standards/sos.

OGC 06-042, OpenGIS Web Map Service (WMS) Implementation Specification, 1.3.0, 2006-03-15, http://www.opengeospatial.org/standards/wms.

OGC 06-121r3 OGC Web Services Common Specification, http://portal.opengeospatial.org/files/?artifact_id=20040.

OGC® 07-000, OpenGIS® Sensor Model Language (SensorML) Implementation Specification, 1.0.0, 2007-07-17, http://portal.opengeospatial.org/files/index.php?artifact_id=21273&passcode=fxphjb8qrca4gwy7g626.

OGC 07-022r1, Observations and Measurements – Part 1 - Observation schema 1.0, 2007-12-08 http://portal.opengeospatial.org/files/?artifact_id=22466.

OGC 07-036 OpenGIS Geography Markup Language (GML) Encoding Standard, 3.2.1, 2007-08-27, http://portal.opengeospatial.org/files/?artifact_id=20509.

OGC 09-001, OpenGIS SWE Service Model Implementation Standard, 2009-09-30.

OGC 09-025r1 and ISO/DIS 19142, OpenGIS Web Feature Service 2.0 Interface Standard, 2010-11-02, http://www.opengeospatial.org/standards/wfs

OGC 09-026r1 and ISO/DIS 19143, OpenGIS Filter Encoding 2.0 Encoding Standard, 2010-11-22, http://www.opengeospatial.org/standards/filter

OGC 10-037, OGC SOS 2 Interface Standard, 2010-09-02, http://www.opengeospatial.org/standards/sos

OGC 10-037, OGC SOS 2 Interface Standard, 2010-09-02, http://www.opengeospatial.org/standards/sos.

OGC 10-126r1, OGC® WaterML2.0: An O&M profile for water observations data, 2010-05-27.

OGC 10-004r2 and ISO/DIS 19156, Geographic information - Observations and measurements,2010-05-03.

OGC 10-025r1, Observations and Measurements - XML Implementation, 2010-11-05.

# Terms and definitions

For the purposes of this report, the definitions specified in Clause 4 of the OWS Common Implementation Specification [OGC 06-121r3], clause 4 of Sensor Observation Service [OGC 06-009r6], and Clause 4 of Observations and Measurements – Part 1 [OGC 07-022r1].

# Conventions

## Abbreviated terms

API   			Application Programming Interface

CSIRO			Australian Commonwealth Scientific and Research Organization

CUAHSI		Consortium of Universities for the Advancement of Hydrologic Science

GSC			Geological Survey of Canada

GML 			Geography Markup Language

GW IE			OGC Groundwater Interoperability Experiment

GWML 		Groundwater Markup Language

HDWG			OGC Hydrology Domain Working Group

ISO    			International Organization for Standardization

KML			Keyhole Markup Language

NCSA			National Center for Supercomputing Applications, U Illinois Urbana

OGC  			Open Geospatial Consortium

OWS 			OGC Web Services

O&M 			Observations and Measurements

SensorML  		Sensor Model Language

SOS 			Sensor Observation Service

SWE 			Sensor Web Enablement

UML 			Unified Modeling Language

USGS			US Geological Survey

WaterML 2 		Water Markup Language

WMC			Web Mapping Context

WMS 			Web Mapping Service

WFS 			Web Feature Service

XML 			eXtensible Markup Language

XSD			XML Schema Definition

UML notation

Class diagrams that appear in this report are presented using the Unified Modeling Language (UML) static structure diagram, as described in Subclause 5.2 of [OGC 06-121r3].

# SWIE Overview

## Background

## Motivation and Goals

This interoperability experiment will advance the development of WaterML2, test its use with various OGC service standards (SOS, WFS, WMS and CSW) and emerging clients.

## User Scenarios

# Use Cases

General description of use cases, followed by detailed descriptions of each use case

## Use Case 1

### Contributors

| Role | Contributor |
| --- | --- |

### Description

### Goals

## Use Case 2

### Contributors

| Role | Contributor |
| --- | --- |

### Description

### Goals

## Use Case 3

### Contributors

| Role | Contributor |
| --- | --- |

### Description

### Goals

Use Case Architecture

## Use Case 1

### Motivation and Goals

### Design and Implementation

### Architectural issues and recommendations

## Use Case 2

### Motivation and Goals

### Design and Implementation

### Architectural issues and recommendations

## Use Case 3

### Motivation and Goals

### Design and Implementation

### Architectural issues and recommendations

# SWIE Best Practices AND outstanding issues

## SWIE Services Profile

Example below.

GWIE-compliant SOS services SHALL use the SOS 1.0 specification, even if the resulting Observation collection is GML 3.2.

## Issues and Recommendations

Example:

SOS GetCapabilities

The SOS 1 specification demands that the list of features-of-interest be explicitly serialized in the GetCapabilities document. This list is either used for discovery (harvesting by catalog) or to provide a valid list of feature identifiers to be used in GetObservation (the feature-of-interest id being one of the parameters of this operation).

SOS 2 has a relatedFeature property (no more information is provided, beside the property cardinality in Table 17 of OGC 10-037), which seems to play a slightly more restricted role.

The Capabilities document of SOS 2.0 lists related features instead of all features-of-interest. The related features are selected by the service provider and serve discovery purposes.

In the current WaterML2 model, it has been decided that the feature-of-interest should be the monitoring station (or any other relevant sampling feature). But, some systems can contain large quantities of features-of-interest, so it is impractical for performance reasons to serialize them individually.

Nonetheless, the service must still need to publish a collection of feature-of-interest that can be used in GetObservation to extract observation related to a specific feature-of-interest.

Proposed Solution

We propose that the profile element SOS5 be fomally part of the SOS specification. The capabilities document should be allowed to provide a composite feature as feature-of-interest. The composite feature shall be a gml:FeatureCollection nesting other gml:FeatureCollections. The collection would be composed of a list of sub-collections. If the sub-collection contains a reasonable amount of features-of-interest, the list would be serialized explicitly; otherwise the composite feature is serialized. The nesting logic within collections is up to the server. It can follow a purely geometric partitioning (e.g. quad-tree) or follow an administrative structure (state/county/city/zip).

## SWIE WaterML 2 Profile

The WaterML 2 Profile used by the SWIE is shown below in Figure 2.

# SW IE Client Implementation

Client 1 - Organsation

### Motivation and goals

### Design and Implementation

### Results

### Issues

Client 2

### Motivation and goals

### Design and Implementation

### Results

### Issues

.

# Acknowledgements

The SWIE is grateful for the invaluable guidance provided by the OGC, and for the commitment and dedication of SWIE participants.