# OGC Project Document XX-XXX: 
Activity Plan for an OGC Interoperability Experiment

Title:	Water Standards Interoperability Experiment

Abbreviation:  WSIE

# Summary

There is a lot of water information and tools in Europe but fragmentation and a lack of coordination between countries exists. The European Commission and the member states have financed several research and innovation projects in support of the Water Framework Directive. Only a few of them are using the recently emerging Hydrological standards, such as OGC WaterML 2.0, and there is a lack of interoperability between tools making the adoption of them difficult. The purpose of this experiment is to assess the difficulty of applying OGC standards in the Water community and to demonstrate their applicability. This experiment will also identify potential gaps in OGC standards. The demonstrated solution will combine different geospatial standards as defined by the Open Geospatial Consortium (e.g., WaterML 2.0, SOS, WPS, WFS, WCS, etc.). The region of interest of this experiment is the Scheldt river basin in Europe.

# INITIATORS ORGANIZATIONS

The OGC members that are acting as initiators of the Interoperability Experiment are:

- Universitat Autonoma de Barcelona - CREAF

- 52° North GmbH

- TU Delft

- Adelphi

- Antea Group

Contact information for initiator organizations is contained in an Annex.

# Participant ORGANIZATIONS

The following organizations will be participating in the GSW IE.

- Universitat Autonoma de Barcelona - CREAF

- 52°North

- A complete list of participating organizations will be added after the 30-day Participation Notification period ends.

Contact information for participant organizations is contained in an Annex. Other organizations and their contributions, as they come onboard, will be updated in the OGC Web Portal project and in the WaterInnEU portal.

The WaterInnEU Horizon 2020 project is providing initial participants to the initiative but the participation of external parties if encouraged. Participants are expected to get visibility, get support to integrate their solutions in the WaterInnEU marketplace. The Engineering Report (ER) resulting from this experiment will shoe their contributions and capacity and will be exposed as a public ER in the OGC website. It will help them to evaluate new technologies. Their participation will be shown the beginning and ate the end of the video demonstration that will be produced as a result.

# DESCRIPTION

The primary focus of this IE is to demonstrate the applicability of OGC standards for the water domain, as follows:

- Applicability of WaterML 2.0 to Scheldt river basin. Use of SOS 2.0 Hydrology Profile for providing WaterML 2.0 data access.

- Combination of WaterML 2.0 and WPS 2.0 to execute flooding modeling.

- Download and presentation of Water models results.

- Alerting/notification services

The desired outcome of this IE is to:

- Successfully demonstrate that OGC standards are applicable in water domain in Europe and assess the difficulty of migrating current tools to the OGC WaterML 2.0 exchange format.

- If areas are identified in the IE where OGC standards have gaps attempt to develop a technical solution to resolve the incompatibility and rerun that portion of the experiment to successfully demonstrate the new approach compatibility and support for the areas previously shown not to be supported.

- Move forward in the Service Notification mechanisms.

## Background

WaterInnEU is a Horizon 2020 project focused on creating a marketplace to enhance the exploitation of EU funded ICT models, tools, protocols and policy briefs related to water and to establish suitable conditions for new market opportunities based on these offerings. Its second primary goal is to assess the level of standardization and interoperability of these outcomes as a mechanism to integrate ICT-based tools, and incorporate open data platforms and generate a palette of interchangeable components that are able to use the water  data emerging from the data sharing processes and data models stimulated by initiatives such as the INSPIRE directive.

As part of this the standardization and interoperability activities in the project, this experiment is designed to demonstrate how current ICT-based tools and water data can works in combination with geospatial web services. The results of the experiment will be documented in an engineering report, and may result in change requests to OGC standards as appropriate. Participants in the IE are expected to contribute to the engineering report. In addition, the artifacts from this experiment will be used as a basis for future deliverables in the WaterInnEU project. These deliverables will be made available to the community. It can also result in some OGC standardization best practice document or a new extension or profile for OGC standards (e.g. a water profile for WPS 2.0).

## Use Case

The specific use cases we want to test include:

- Extract data from river gauges data in OGC WaterML 2.0 format using SOS services (preferably compliant to the OGC SOS 2.0 Hydrology Profile Best Practice).

- Model floods using a WPS 2.0 and WaterML 2.0 data as input.

- Evaluate the applicability of Sensor Notification Services (interface to be defined) in water emergencies

## Scenario

An extreme weather situation is forecasted. River gauges data is continuously monitored. An increase in water flow is detected. Flooding models are executed and affected areas are determined. Emergency services are mobilized, lives are saved and damages on property and crops are estimated.

## Data

The following data will be available for the Interoperability experiment:

- Height/flow data form a past similar event

- Inhabited areas, population data, value of property crops, etc.

- TBD

## Experiments

The IE will attempt to address the following experiments:

- Experiment #1: Extract WaterML 2.0 from the SOS 2.0 Hydrology Profile for the desired area and time

- Experiment #2: If the readings exceed a threshold, start a WPS 2.0 execution with a hydrological model.

- Experiment #3: Expose the results of the model using geospatial services for download a visualization.

- Experiment #4: Notify alerts to the relevant emergency services using Sensor Notification Services or similar. This might be more experimental, since there is a lack of official standards. Current work of the OGC Pub/Sub Standards Working Group can be an alternative to take into consideration.

# TECHNICAL APPROACH

The Technical Approach for this Interoperability Experiment focuses on leveraging existing OGC Specifications and, as needed, developing change requests for these specifications. The following section describes the Technical Approach in detail.

## Experimental Methodology

Experiment overview:

The architecture will test the combination of Gauge data in a WPS that will be triggered by a meteorological alert. The data will be translated into OGC WaterML 2.0 time series data format and will be ingested in a SOS 2.0. SOS data wil be visualized in a SOS Client that is able to handle time series. The meteorological alert (with the supervision of an operator (manipulating the WPS user interface) will trigger the execution of a WPS that will ingest WaterML 2.0 time series and terrain data etc that will be input for a flooding modeling algorithm. The WPS will be able to produce flooding datasets in the form of coverages that will be the offered to clients via a WCS 2.0 service or a WMS 1.3 service, and downloaded and visualized by the respective clients. The WPS will trigger a notification or an alert that will be monitored from a emergency control response.

## Demonstration Planning

The intent is to provide a flexible environment for demonstration based on the precise requirements of participating members. Minimally, a windows environment will be made available for experimentation.  The exact configuration of onsite and offsite hardware, as well as vendor software will be designed based on the specific participants involved.

## Specification Development

The primary focus of this IE will be WaterML and SOS, and a secondary focus will be WPS. Resulting interface definitions will then be considered for change requests against existing OGC standards. The list of specifications that may be affected includes:

- SOS (preferably OGC SOS 2.0 Hydrology Profile)

- WPS (preferably OGC WPS 2.0)

- WaterML 2.0

## Component Development

The following components will be developed concurrently by the responsible organization(s), to be completed by the execution end date.

| Description | Sponsor / Implementor(s) |
| --- | --- |
| WaterML 2.0 translator | CREAF |
| SOS compatible with Water ML 2.0 model and implementing the OGC SOS 2.0 Hydrology Profile Best Practice | 52°North |
| WPS 2.0 with WaterML2.0 input | CREAF |
| Sensor Notification Service | 52°North |
| WFS, WMS Server | TBD |
| SOS Client/viewer | 52°North |
| WPS Client interface | 52°North |
| Visualization client | CREAF |
| Notification client | TBD |

Other related services/clients that will be included:

| Description | Sponsor / Implementor(s) |
| --- | --- |

## Testing and Integration

Establish a virtual test bed at CREAF

Establish requirements for access

TWiki provided by OGC for collaboration

Testing and integration will largely involve implementation of the of the demonstration use case.

Establish a test plan and metrics to test objectives and use cases documented in this activity plan as appropriate.

Two face-to-face testing and integration sessions will be proposed, once at the beginning of the testing and integration period and once directly prior to the demonstration.

# DELIVERABLES

The documentation listed below will be considered the deliverable for the project.

## Documentation

The following documentation will comprise the deliverables for the project. All artifacts and results associated with experiment will be made available to OGC members.

Engineering Report discussing the details and results.  Report will include but not be limited to summaries of the activity plan, test plan et al supporting documentation as appropriate

Change Requests for OGC Specifications as appropriate

Candidate Water OGC Best Practices as appropriate

Include change requests for OGC specifications as appropriate

## Demonstration

An Internet demonstration of all functioning components will be made towards the end of the IE.

This demonstration will be made persistent using the resources of OGC Network.

# SCHEDULE (Tentative)

Startup Activity Plan submission: September 30th, 2015 OGC Review Board approval: October 31st, 2015 Start of participation notification period: November 15th, 2015

Execution Planned kickoff date: January 8th, 2016 (30-day post press release) Development, testing and bug fixing January – June 2016 Planned end date: June 30th, 2016

Wrap-up and Reporting Technology Demonstration June 2016 Final report submission August 2016

Note: Additional milestone dates will be added at the kickoff meeting.

# RESOURCE PLAN

The Initiative Manager will be Joan Masó, and the Initiative Technical Lead will be Lluis Pesquer, CREAF.  The OGC Initiative Facilitator will be Lewis Leinenweber.

The following resources will be available.

| Staffing | CREAF will provide sufficient resources to ensure the main thread of this IE is completed in accordance with the requirements of this activity plan and supporting documentation. The other initiators agreed to support this activity to the degree necessary to ensure the completion of this IE. Participants will provide sufficient resources to ensure completion of their agreed upon area of this experiment in accordance with this activity plan and supporting documentation. |
| --- | --- |
| Software | As needed, mainly open-source tools, services, and client applications. |
| Other Resources | Machine, software and technical resources available CREAF |

# REQUIREMENTS FOR PARTICIPATION

In order to become a participant in this IE, an organization must be willing make a resource commitment to make a substantial contribution in one or more of the following areas:

An OGC service component exposing its resources, or

a consumer application that can use the OGC service to exploit the data, or

testing of the Services/Clients, or

a server to house a IE component, or

data to support the IE Demonstration, or

compilation of documentation into one or more of the Interoperability Experiment deliverables (note that all participants must also provide sub-reports for inclusion in the final reports)

# INITIATOR ORGANIZATIONS – Contact Information

| Organization Name | Universitat Autonoma de Barcelona - CREAF |
| --- | --- |
| Business Contact | Name | Joan Masó |
|  | Title | Researcher |
|  | Street Address | Edifici C, UAB, 08913 Bellaterra (Bercelona), Spain |
|  | Email Address | Joan.Maso@uab.cat |
|  | Phone | +34 93 581 1771 |
|  | Fax | +34 93 581 4151 |
| Technical Contact | Name | Lluis Perquer |
|  | Title | Researcher |
|  | Street Address | Edifici C, UAB, 08913 Bellaterra (Bercelona), Spain |
|  | Email Address | Joan.Maso@uab.cat |
|  | Phone | +34 93 581 2666 |
|  | Fax | +34 93 581 4151 |

| Organization Name | 52°North GmbH |
| --- | --- |
| Business Contact | Name | Christoph Stasch |
|  | Title | Researcher, Project Manager |
|  | Street Address | Martin-Luther-King-Weg 24 |
|  | Email Address | c.stasch@52north.org |
|  | Phone | +49 251 396 371 32 |
|  | Fax | +49 251 396 371 11 |
| Technical Contact | Name | Eike Hinderk Juerrens |
|  | Title | Researcher, Software Developer |
|  | Street Address | Martin-Luther-King-Weg 24 |
|  | Email Address | e.h.juerrens@52north.org |
|  | Phone | +49 251 396 371 33 |
|  | Fax | +49 251 396 371 11 |

# Participant ORGANIZATIONS - Contact Information

| Organization Name | Universitat Autonoma de Barcelona - CREAF |
| --- | --- |
| Business Contact | Name | Joan Masó |
|  | Title | Researcher |
|  | Street Address | Edifici C, UAB, 08913 Bellaterra (Bercelona), Spain |
|  | Email Address | Joan.Maso@uab.cat |
|  | Phone | +34 93 581 1771 |
|  | Fax | +34 93 581 4151 |
| Technical Contact | Name | Lluis Perquer |
|  | Title | Researcher |
|  | Street Address | Edifici C, UAB, 08913 Bellaterra (Bercelona), Spain |
|  | Email Address | Joan.Maso@uab.cat |
|  | Phone | +34 93 581 2666 |
|  | Fax | +34 93 581 4151 |

| Organization Name | 52°North GmbH |
| --- | --- |
| Business Contact | Name | Christoph Stasch |
|  | Title | Researcher, Project Manager |
|  | Street Address | Martin-Luther-King-Weg 24 |
|  | Email Address | c.stasch@52north.org |
|  | Phone | +49 251 396 371 32 |
|  | Fax | +49 251 396 371 11 |
| Technical Contact | Name | Eike Hinderk Juerrens |
|  | Title | Researcher, Software Developer |
|  | Street Address | Martin-Luther-King-Weg 24 |
|  | Email Address | e.h.juerrens@52north.org |
|  | Phone | +49 251 396 371 33 |
|  | Fax | +49 251 396 371 11 |

| Organization Name | Other Organizations |
| --- | --- |
| Business Contact | Name |  |
|  | Title |  |
|  | Street Address |  |
|  | Email Address |  |
|  | Phone |  |
|  | Fax |  |
| Technical Contact | Name |  |
|  | Title |  |
|  | Street Address |  |
|  | Email Address |  |
|  | Phone |  |
|  | Fax |  |

# ACRONIMS

CR	Change Request

ER 	Engineering Report

OGC	Open Geospatial Consortium

AS	Alert Service

ES	Event Service

ICT	Information and Communication Technology

IE	Interoperability Experiment

NS	Notification Service

SOS	Sensor Observation Service

WaterML	Water Markup Language

WCS 	Web Coverage Service

WMS 	Web Map Service

WPS 	Web Processing Service

# Footnotes

Even if there has been considerable work done for the definition and testing of Alert/Notification services, there is no OGC official standard that is specifying this yet.

# Text boxes

WaterML translator

WaterML SOS

WaterML WPS

WCS

WMS

Notification/Event Services

Meteo

alert

WPS user interface

SOS WaterML client

Visualization client

Emergency response control

Services

Clients

Gauge

data source