## Slide 1: Inspire O&M & SWE requirements - profile
BRGM – S.Grellet
52N – S.Jirka

## Slide 2: Context
Several INSPIRE themes refer to O&M & SWE
  Geology
  Oceanographic geographical features and Sea Regions
  Atmospheric conditions and Meteorological geographical features
  Environmental monitoring facilities
  Soil
First guidelines document produced in 2011 (slightly updated in 2013)
  Current V2 version : http://inspire.jrc.ec.europa.eu/documents/Data_Specifications/D2.9_O&M_Guidelines_v2.0.pdf
  Current running contracts (BRGM and 52N) to, respectively,
    update guidelines document (D2.9) and recommendation for SOS as an Inspire download service
    and provide the corresponding reference implementation
Notes: 2
2

## Slide 3: Context
Inspire maintenance group
  Set up with experts from various EU organisations
  Identifies implementation UseCases
  Provides feedback on previous guidelines document
Objective
  Refine the guidelines document (D2.9) based on inputs above
  Push it as an OGC profile
  Refine the INSPIRE SOS dowload service technical guidance
  Better link together the two documents
Notes: 2
2

## Slide 4: O&M Design patterns
Decision tree
  Screenshot
  from the previous
  one
Leading to specialisedObservations
  Most of which derived from OM_DiscreteCoverageObservation
Notes: 2
2

## Slide 5: O&M Design patterns
specialisedObservation example
  PointTimeSeries
/req/inspire-om-design-patterns/pointTimeSeriesObservation | When the Observation represents a time-series of point measurements of a property at a fixed location in space the specialised observation ‘PointTimeSeriesObservation’ SHOULD be used
An example of such case could be an air quality monitoring station providing hourly ozone measurements.
The featureOfInterest represents the direct surrounds of the air intake (i.e. the air bubble surrounding the air intake).
The location for the measurements is provided through this featureOfInterest.
As this design pattern usually provides a time series (temporal coverage) result,
the phenomenonTime and/or resultTime will often be provided together with the result values.
Notes: 2
2

## Slide 6: O&M Design patterns
specialisedObservation
  PointTimeSeries
Notes: 2
2

## Slide 7: O&M Design patterns
Other specialised observations
  point, multiPoint, pointObservationCollection
  profile & trajectory
  grid & gridTimeSeries
  specimen & specimenTimeSeries (under discussion)
Notes: 2
2

## Slide 8: O&M profile
Core Observation profile
  Requirement classes : most of them are recommendation (only few are requirements)
  OM_Observation : identifier, time (ISO 8601)
  observedProperty :
    communityVocabulary, SKOS
    observableProperty (inspired from CSML3 : Dominic Lowe - British Atmospheric Data Centre – BADC) initially recommended (in V2) : few implementation feedback available -> moved to informative annex.
  featureOfInterest :
    SF_SamplingFeature ,
    provision of sampledFeature : either domain feature or Nasa SWEET entry
    pattern for depth/elevation provision
Notes: 2
2

## Slide 9: O&M profile
Core Observation profile
  Procedure
    sensorType not instance (as in SOS hydro profile)
    dedicated Process specialisation in Inspire (xsd and mapping to SensorML)
  Link to monitoringFacility or monitoringNetwork generating the observation :
    Pattern defined using om:parameter. With value pointing to URI of the facility/network
Metadata
  No clear need identified
Notes: 2
2

## Slide 10: O&M profile
Result encoding
  TimeSeriesML support: issue to be clarified is the backward compatibility with WaterML2 (specialised observation use it)
  JSON encoding to OM
  Need for a resultType information ?
    Especially for out-of-band results
    So that the client knows before retrieving the observation result its type
    A discussion paper was produced during the previous work phase.
    No decision was taken so far.
    Attached in an informative annex to the document produced
Notes: 2
2

## Slide 11: Service Layer
Work on updating GetDataAvailability
  SOS hydrology profile
  Adding offeringID and observationType in the response
Notes: 2
2

## Slide 12: Service Layer
Recommended service patterns (WFS / SOS)
  1°/ WFS : access Monitoring Facility/Network description
  2°/ SOS: getDataAvailability to test ground for observation available at the monitoring feature level
  retrieve offeringID
  3°/ SOS: getObservation on a given OfferingID
Notes: 2
2

## Slide 13: Technical guidelines for SOS as an INSPIRE download service
Extended capabilities for metadata
Mapping Inspire terminology to SOS operations
  Ex : INSPIRE dataset -> Offerings
Remaining points
  DescribeSensor operation behaviour to be confronted to Inspire Enviromental Monitoring Facilities theme
  Observation identifier handling : getObservationById should reuse gml:identifier. Inspire ‘identifier’ is a dedicated type that is not gml:identifier…
Notes: 2
2

## Slide 14: Next steps
Gather more profiles
  New Zealand Environmental Observation Data Profile
  Environment Canada Common Observation and Measurement Profile (nealy collected)
  More ?
Communicate
  Raise awareness at this TC : SWE DWG, HydroDWG
  In between both TCs : circulate document to gather comments
  Next TC (Dublin) : discuss into more details. SWE ? HydroDWG ?
Notes: 2
2

## Slide 15: Thank you
s.grellet@brgm.fr
jirka@52north.org
Notes: 2
2