Open Geospatial Consortium

Date: 2012-07-31

External identifier of this OGC® document: <http://www.opengis.net/doc/template/standard/1.0>

Internal reference number of this OGC® document: 12-nnnr1

Version: 0.3.4.2

Category: OGC® Best Practice

Editor: <Name(s) of Editor or Editors>

Best Practices for using OGC WMS with Time-Dependent or Elevation-Dependent Data

Copyright notice

Copyright © 2012 Open Geospatial Consortium
To obtain additional rights of use, visit http://www.opengeospatial.org/legal/.

Warning

This document is not an OGC Standard. It is distributed for review and comment. It is subject to change without notice and may not be referred to as an OGC Standard.

Document type:   	OGC® Publicly Available Best Practice

Document subtype:   	<interface, encoding, application profile, profile>

Document stage:   	Draft

Document language: 	English

Recipients of this document are invited to submit, with their comments, notification of any relevant patent rights of which they are aware and to provide supporting documentation.

Abstract

This document proposes a set of Best Practices and some guidelines for implementing and using the OGC Web Map Service (WMS) to serve maps which are time-dependent or elevation-dependent. In particular, clarifications or restrictions on the use of WMS are defined to allow unambiguous and safe interoperability between clients and servers, both in the context of expert meteorological and oceanographic usage and in other communities using meteorological and oceanographic information in conjunction with their own domains’ data. This Best Practice applies specifically to WMS version 1.3, but many concepts and recommendations herein will be applicable to other versions of WMS or to other OGC services, in particular the Web Coverage Service.

Where strict normative conformance has been identified, this is indicated, with reference to the original standard.

Keywords

The following are keywords to be used by search engines and document catalogues:

ogcdoc, WMS, 1.3, web map service, meteorology, oceanography, time, elevation.

Preface

Attention is drawn to the possibility that some of the elements of this document may be the subject of patent rights. The Open Geospatial Consortium shall not be held responsible for identifying any or all such patent rights.

Recipients of this document are requested to submit, with their comments, notification of any relevant patent claims or other intellectual property rights of which they may be aware that might be infringed by any implementation of the standard set forth in this document, and to provide supporting documentation when possible.

Submitting organizations

The following organizations submitted this Document to the Open Geospatial Consortium Inc.

DWD (Deutscher Wetterdienst)

ECMWF (European Centre for Medium-range Weather Forecasts)

Météo-France

Technische Universität Dresden

UK Met Office

US Navy

US NOAA (National Oceanic and Atmospheric Administration)

Submitters

All questions regarding this submission should be directed to the editor or the submitters:

| Name | Company |
| --- | --- |
| Chris Little | UK Met Office |
| Marie-Françoise Voidrot-Martinez | Météo-France |
| Jeff de La Beaujardière | US NOAA |
| Stephan Siemen | ECMWF |
| Roy Ladner | US Navy |
| Jürgen Seib | DWD |

More generally, these Best Practices are the result of discussions within the OGC Meteorology and Oceanography Domain Working Group and the OGC Technical Committee.

# Introduction

The meteorological and oceanographic communities have been exchanging information internationally for at least 150 years and very well understand the importance of geospatial interoperability standards encompassing standardized data formats, interfaces and processes; shared conceptual models; and stable, sustainable, maintenance processes and institutions.

Because of the demanding nature of meteorological and oceanographic data processing, the communities have evolved domain specific solutions. As computers have become more powerful, it has become feasible to use general geospatial software for day-to-day operational purposes, and interoperability problems have arisen. There is also an increasing need to combine meteorological and oceanographic data with other forms of geospatial data from other domains, in ways convenient for those domains.

This document describes and justifies a set of Best Practices for implementing Web Map Service (WMS) servers and clients to meet the interoperability requirements of the meteorological and oceanographic communities and to promote the economies of using Commercial Off-The-Shelf geospatial software.

1.1 Time

Meteorological and oceanographic data may be associated with zero, one or two temporal axes.

1.1.1 For example, a topographic base layer may have no associated time axis.

1.1.2 A satellite imagery layer may have one time axis with images available at one or more validity times.

1.1.3 A numerical weather forecast calculation, a series of alerts and data associated with trajectories of moving objects may have two time axes that present complex dimensional dependencies.

1.1.4 For a certain forecast calculation, assume three separate calculations for air temperature, each containing 48 forecasts at successive 1 hour intervals. The available combinations of validity time and calculation nominal start time will be as shown in the table below. Columns sharing an “*” across rows indicate forecasts from different calculations that share the same valid time. These might be represented in a WMS as 48 separate layers or as a single layer with two time dimensions. The former approach will result in a larger, more complex capabilities document; the latter approach will permit the combinations to be expressed more compactly as a single layer.

|  | Validity Time of Forecasts |
| --- | --- |
|  | 2009-11-26 | 2009-11-27 | 2009-11-28 |
| Nominal Start Time | 00-12 | 12-00 | 00-12 | 12-00 | 00-12 | 12-00 |
| 2009-11-26T00:00 | * | * | * | * |  |  |
| 2009-11-26T12:00 |  | * | * | * | * |  |
| 2009-11-27T00:00 |  |  | * | * | * | * |

Table 1: Example of Two Dimensional Time Axes for Numerical Model Forecast Data

1.1.5 Data associated with alerts or warnings often have multiple time axes. The Common Alerting Protocol (CAP), for example, provides for warnings that may have four time attributes:

    - Sent time: the date and time of the origination of the warning.

    - Effective time: the effective time of the information of the warning.

    - Onset time: the expected time of the beginning of the event in the warning.

    - Expiration time: The expiry time of the information of the warning

In several CAP implementations for meteorological warnings, “sent time” is equal to “effective time”. The “validity duration” of the message is the period between “onset time” and “expiration time”. If CAP files with meteorological warnings are produced periodically (e.g. every 5 minutes), then a warning may exist in more than one CAP file. The “sent time” can be used to distinguish them using a Dimension specification in the map layers.

1.1.6 A trajectory is the path that a moving object follows through space as a function of time. In meteorology, trajectories are often observed or computed periodically. A data provider may then have a set of trajectories with different starting times. The trajectory data and map layers are distinguished by their “start times”.

1.2 Elevation

Meteorological and oceanographic data may also be associated with no defined elevation, single defined elevation, multiple elevations on a well-defined axis and elevation derived from computed surfaces.

1.2.1 For example, a topographic base layer may have no associated elevation.

1.2.2 Data having multiple elevations might be represented in a WMS as multiple separate layers or as a single layer with a single elevation dimension expressing each elevation value.

1.2.3 Data at mean sea level is expressed on a computed surface.

This document describes a set of best practices for implementing these time and elevation dependencies in WMS servers and clients.

# Scope

This application profile document describes best practices for WMS layers and dimensions for time-dependent and elevation-dependent meteorological and oceanographic data.  It describes how WMS layers and dimensions for time and elevation should be used to manage meteorological and oceanographic metadata in WMS Capabilities Documents.  This document establishes Best Practices for available values on time and elevation dimension axes in the context of:

- Server (Capabilities Document) and client (GetMap request) rules,

- Cases for zero, one or two overlapping time axes, and

- Cases for the elevation axis with no defined elevation, single defined elevation, continuous monotonic elevation and elevation derived from computed surfaces.

This OGC document specifies a constrained, consistent interpretation of the WMS 1.3 standard that is applicable to government, academic and commercial providers of meteorological and oceanographic Web map products.

These Best Practices currently do not encompass the specification of climatological periods, ranges, processing or special calendars, but it is envisaged that they will be extended to cover these topics.

It is envisaged that these Best Practices could be considered for future versions of WMS and other OGC standards.

# References

The following normative documents contain provisions that, through reference in this text, constitute provisions of this document. For dated references, subsequent amendments to, or revisions of, any of these publications do not apply. For undated references, the latest edition of the normative document referred to applies.

OpenGIS® Web Map Server Implementation Specification Version 1.3.0. 2006-03-15. http://portal.opengeospatial.org/files/?artifact_id=14416

ISO 8601:2004, Data elements and interchange formats — Information interchange — Representation of dates and times

CAP Common Alerting Protocol Version 1.2, OASIS Standard, 2010-07-01. http://docs.oasis-open.org/emergency/cap/v1.2/CAP-v1.2-os.html

# Terms and Definitions

This document uses the terms defined in Sub-clause 5.3 of [OGC 06-121r8], which is based on the ISO/IEC Directives, Part 2, Rules for the structure and drafting of International Standards. In particular, the word “shall” (not “must”) is the verb form used to indicate a requirement to be strictly followed to conform to this Best Practice.

For the purposes of this document, the following additional terms and definitions apply.

4.1

client

software component that can invoke an operation from a server

4.2

geographic information

information concerning phenomena implicitly or explicitly associated with a location relative to the Earth [ISO 19101]

4.3

interface

named set of operations that characterize the behaviour of an entity [ISO 19119]

4.4

layer

basic unit of geographic information that may be requested as a map from a server

4.5

map

portrayal of geographic information as a digital image file suitable for display on a computer screen

4.6

operation

specification of a transformation or query that an object may be called to execute [ISO 19119]

4.7

portrayal

presentation of information to humans [ISO 19117]

4.8

request

invocation of an operation by a client

4.9

response

result of an operation returned from a server to a client

4.10

server

a particular instance of a service

4.11

service

distinct part of the functionality that is provided by an entity through interfaces [ISO 14252]

4.12

validity time

# Abbreviated terms

CAP 		Common Alerting Protocol

CRS 		Coordinate Reference System

GIS 		Geographic Information System

GRIB 		GRidded Binary data format

IEC 		International Electrotechnical Commission

ISO 		International Standards Organisation

OGC 		Open GIS Consortium

Met Ocean 	Meteorology and Oceanography

URL 		Uniform Resource Locator

WMS 		Web Map Service

XML 		eXtensible Markup Language

# Conventions

This sections provides details and examples for any conventions used in the document. Examples of conventions are symbols, abbreviations, use of XML schema, or special notes regarding how to read the document.

Any keywords from the WMS Standard are depicted in UPPER CASE, even if lower case is allowed by the Standard.

Any keywords specified by this Best Practice are depicted in lower case, non-italic.

Any example values for keywords from the WMS Standard or this Best Practice are depicted in lower case italic.

# Requirements for WMS Meteorology and Oceanography services

This section highlights best practices for use of time in WMS.  Generally, WMS 1.3 defines two dimensions, TIME and ELEVATION, and offers a generic way to add further dimensions.

The TIME dimension is defined as <Dimension name="TIME">.  A corresponding GetMap request includes TIME=t.

The ELEVATION dimension is defined as  <Dimension name="ELEVATION">.  A corresponding GetMap request includes ELEVATION=z.

Provider-defined "sample dimensions" are defined as <Dimension name="something">. A corresponding GetMap request includes DIM_something=value.

## WMS Layer – General Handling of Time

In all cases, the dimension TIME shall be used in accordance with the following guidelines:

- The dimension TIME shall be used to specify validity time (e.g., of an observation or forecast).

- The dimension TIME shall be used to aggregate data sharing a common time axis as a single Layer with zero or more TIME axes. This will avoid multiple independent but time related layers, possibly with time encoded in the Layer Name.

- The date/time format shall follow the following format to appropriate precision: ccyy-mm-ddThh:mm:ss.sssZ.

- Multiple times may be expressed either as a list or as a start/end/interval in accordance with WMS 1.3, Table C.2.

- The units shall be ISO8601:2000 and specified as an attribute in the layer as units="ISO8601.” This includes the time zone

Climatological intervals and temporal references will be the subject of future work and may not use strict ISO 8601. Multiple times may be expressed either as a list or as a start/end/interval, as shown in WMS 1.3 Table C.2.

### WMS Layer – No defined Time

Validity time is not relevant to some data such as topographic layers or climatological normals.  In such cases, the dimension TIME shall be used in accordance with the following guidelines

- The Layer shall not declare a TIME value.

- The layer shall avoid inheritance of TIME from parent layers.

- TIME included in a GetMap request shall be ignored.

### WMS Layer – Single Time axis

For data with one or more available times along a single time axis, the dimension TIME shall be used in accordance with the following guidelines:

- The TIME dimension shall specify time values {Ti} either as a list (T0, T1, ... TN) and/or range (T0/T1/ΔT) in accordance with WMS 1.3, Table C.2.

- The attribute CURRENT shall be used, and, if the data are continually updated, shall be set to true.

- The attribute DEFAULT shall be used and set to the validity time that will be used if the GetMap request does not specify a time.

- The attribute NEARESTVALUE shall be used and set to true, advertising that the nearest available time to that specified in the GetMap request will be used.

- Use of the attribute MULTIPLEVALUES is optional.  Where the data provider supports animations or mash-ups of multiple layers, the attribute SHALL be used and set to true.  Submission of multiple GetMap requests is recommended where the user cannot tolerate one or more layers in an animation or mash-up that was included based on a NEARESTVALUE attribute vice a precise match.

- Specification of TIME in GetMap requests is recommended.

Figure 1: Decision tree to analyze Time in GetMap request.

### WMS Layer – Double Time Axes

For data with one or more available times on two time axes, the dimension TIME shall be used in accordance with the following guidelines:

- The TIME dimension shall be used to specify validity times.

- The dimension name “reference_time” shall be used to specify second time axis.  The second time axis to which it refers shall be specified in the Layer abstract.

- The attribute NEARESTVALUE shall be used and set to true, advertising that the nearest available validity time to that specified in the GetMap request will be used.

- GetMap requests should specify TIME and reference_time.

Figure 3: Decision tree for XXX_Time in GetMap request.

## Vertical Axes in WMS

### General Handling of Elevation

In all cases, the dimension ELEVATION shall be used in accordance with the following guidelines:

- Each Layer may have exactly one ELEVATION axis <Dimension name="elevation">.

- ELEVATION axis shall have a well-defined vertical coordinate reference system (CRS). The name of the CRS must be assigned to the mandatory attribute “units”. It can be either a label or a URL (see Clause 6.7.5).

- Elevations shall be expressed in units of this CRS. If there exists a symbol for these units, then the string representation of this symbol should be given in the attribute “unitSymbol”.

- If an ELEVATION axis is present, then it shall have at least one value.

- A single elevation may be either expressed as a name (e.g. mean sea level), or a number (integer or floating point) or an interval.

- Multiple elevations may be defined either as a list of single elevations or as a min/max/interval, as shown in WMS 1.3 Table C.2.

- ELEVATION shall be used to aggregate data sharing a common vertical coordinate reference system (CRS) as a single LAYER. This will avoid multiple independent layers related by a common CRS.

### WMS Layer – No defined Elevation

Elevation is not relevant to broad number of layers such as topographic layers.  In such cases, the dimension ELEVATION shall be used in accordance with the following guidelines

- The Layer shall not declare an ELEVATION dimension.

- The layer shall avoid inheritance of ELEVATION from parent layers.

- If a GetMap request includes an ELEVATION parameter, then this parameter shall be ignored.

### WMS Layer – One single Elevation

In cases where a layer belongs to exactly one elevation, e.g. the temperature on mean sea level, the dimension ELEVATION shall be used in accordance with the following guidelines

- The ELEVATION dimension must define one elevation value Z.

- The attributes “nearestValue” and “default” must be set as follows: nearestValue=false, default=Z

- If a GetMap request includes an ELEVATION parameter, then this parameter may be ignored.

### WMS Layer – Multiple Elevations

For data with one or more available elevations along the elevation axis, the dimension ELEVATION shall be used in accordance with the following guidelines:

- Those properties must be fulfilled by the vertical coordinate reference system (CRS), e.g.:

  - CRS:88 = North American Vertical Datum 1988. unitSymbol=m (see B.5)

  - ? = Geopotential Height. ID & ISO 19111 definition t.b.d. unitSymbol=m.

  - ? = Pressure Level. ID & definition t.b.d. unitSymbol=hPa

  - ? = Flight Level. ID & definition t.b.d. unitSymbol=FL.

- The ELEVATION dimension shall specify elevation values {Zi} either as a list (Z0, Z1,… ZN) and/or range (Z0/Z1/ΔZ) in accordance with WMS 1.3, Table C.2. Some models produce outputs on surfaces with a nonzero vertical thickness (e.g., 1000-900 hPa). Need to be able to express that.

- The attribute “default” shall be used and set to the elevation that will be sent if the GetMap request does not specify an elevation.

- The “nearestValue” attribute shall be used and set to false, advertising that an exception will be submitted if the elevation that is specified in the GetMap will not exist.

- The “multipleValues” attribute shall be used and set to false, because each map usually represents a single elevation.

- Specification of ELEVATION in GetMap requests is recommended.

### WMS Layer – Fixed Surfaces

- Canonical Use Case: Aviation weather products

  - Example: Wind speeds computed for a tropopause, mean sea level, isotherms, base and top of contrail layer, surfaces of constant potential vorticity (PVU), jet level.

  - See http://external.opengis.org/twiki_public/MetOceanDWG/MetOceanWMSBP20120206

- Use <DIMENSION na”e="elevat”on">  to enumerate

  - verticalCRSid“= "computed_surf”ce"

  - units“” "" (null string)

  - unitSymbol“””""" (null string)

  - Element contains comma-separated list of available surfaces, e.g.:

    - <Dimension na”e="elevat”on" verticalCRS”d="computed_surf”ce" uni””="" unitSymb””="">Tropopause, Mean Sea Level, 0.7PVU, Jet_level, Isotherm_T0, 2nd_Isotherm_T0</Dimension>

  - Attributes: nearestValue=false, multipleValues=false, default=name

- Client: ELEVATION=name in GetMap request is used to choose desired surface

The following issues on vertical CRS need to be resolved:

- Community-specific vocabulary(ies) for surface names

  - Code table 4.5 of the GRIB 2 edition defines a list of fixed surface types and units

  - URL: http://rda.ucar.edu/docs/formats/grib2/grib2doc/code4.5.html

- How to handle same quantity available both on computed surfaces and at normal elevation levels

  - Possibly ambiguous or conflicting GetMap requests

- ISO 19111 definitions of common vertical CRSs (pressure, geopotential height, etc)

””–

Annex A: Revision history

| Date | Release | Author | Paragraph modified | Description |
| --- | --- | --- | --- | --- |
| 2012-07-10 | 0.1.0 | CTL | All | First introductory text |
| 2012-07-11 | 0.2.0 | CTL | Annexes added | Added agreed content from presentations |
| 2012-07-25 | 0.2.1 | JdLB |  |  |
| 2012-07-25 | 0.3.0 | SS |  |  |
| 2012-07-26 | 0.3.1 | RL |  |  |
| 2012-07-27 | 0.3.2 | JS |  |  |
| 2012-07-30 | 0.3.3 | CTL | All | Editorial changes agreed by telecon |
| 2012-07-31 | 0.3.4 | CTL, MM | All and Section 7 | Accepted changes: should to must |
| 2012-07-31 | 0.3.4.1 | RL | 1, 1.1.x, 7.1.x | Section 1 – grammatical edits; corrected numbering in 1.1.x; section 7 edits in accord with section 6 conventions; added content to 7.1.2 per July 2 teleconf discussion. |
| 2012-08-06 | 0.3.4.2 | RL | 1.x-7.1.x, 7.2.1 | 1.x-7.1.x - accepted changes and provided edits based on 6 August telecon, added validity time. 7.2.1 – rephrased last sentence. |

Annex B: Bibliography

The World Meteorological Organization (WMO) operational data formats are described here: http://www.wmo.int/pages/prog/www/WMOCodes.html and in particular, the binary gridded data format GRIB  contains many controlled lists of vertical and horizontal CRS, map projections, and parameters used by the meteorological and oceanographic communities which can be found at: http://www.wmo.int/pages/prog/www/WMOCodes/WMO306_vI2/LatestVERSION/LatestVERSION.html .

More general background information can also be found at http://www.wmo.int/pages/prog/www/index_en.html .

Annex of notes, reminders, etc. To be deleted when complete.

Get reviews from Adrian Custer, Joan Maso, WMS telcos, Jeremy Tandy and co.

DECISION: Intercept WMS 1.3. Make new one for WMS2.0.

Triage features into: stay same, need to change, don’t know

Pick up details and examples from MoD Profile

Legend: problematic

DECISION: MUST support PNG for transparency as a minimum. SVG nice. Same as WMS 1.3. then add to abbreviations:

PNG 		Portable Network Graphics

SVG 		Scalable Vector Graphics

DIMENSIONS

Names and title

Keyword list

Styles?

Queryable layers LATER?

Bounding box

CRS

Scale

Data URL ?

Null/negative responses.

Table 1 UNCHANGED

Table 2 UNCHANGED

Table 3 — The parameters of a GetCapabilities request URL

| Request parameter | Mandatory / Optional | Description | Met Ocean Profile |
| --- | --- | --- | --- |
| VERSION=version | O | Request version | M |
| SERVICE=WMS | M | Service type | No change |
| REQUEST=GetCapabilities | M | Request name | No change |
| FORMAT=MIME_type | O | Output format of service metadata | ? |
| UPDATESEQUENCE=string | O | Sequence number or string for cache control | ? |

Table 4 — Use of UpdateSequence parameter UNCHANGED

| Client request UpdateSequence value | Server metadata UpdateSequence value | Server response | Met Ocean profile |
| --- | --- | --- | --- |
| None | any | most recent service metadata | No change |
| Any | none | most recent service metadata | No change |
| equal | equal | Exception: code=CurrentUpdateSequence | No change |
| Lower | higher | most recent service metadata | No change |
| higher | lower | Exception: code=InvalidUpdateSequence | No change |

Table 5 — Relationship between ISO 19128 and ISO 19115 metadata fields

| ISO 19128 layer property | ISO 19115 Metadata element | Relationship |  |
| --- | --- | --- | --- |
| Title | CI_Citation.title | equivalent | Check WMO core Profile |
| Abstract | MD_DataIdentification.abstract | equivalent | Check WMO core Profile |
| Keyword element inKeywordList | MD_TopicCategoryCode | equivalent if “vocabulary” attribute of 19128 <Keyword> element is “ISO 19115:2003”. Other vocabularies are permitted by 19128. | Check WMO core Profile |
| EX_GeographicBoundingBox | EX_GeographicBoundingBox | equivalent | No change |
| CRS | MD_CRS | Value of CRS in 19128 is a text string that identifies a coordinate reference system defined by another authority. Value of MD_CRS in 19115 is a list of projection, ellipsoid and datum identifiers. | ?? |
| BoundingBox | EX_BoundingPolygon | 19128:BoundingBox is strictly a box (lower left and upper right corners in a specified CRS). 19115:EX_BoundingPolygon may be a polygonal boundary. | ?? |
| Attribution | CI_ResponsibleParty | Title element of 19128:Attribution is equivalent to organisationName element of 19115: CI_ResponsibleParty. Other elements of 19128:Attribution have no equivalent in 19115. | Check WMO core Profile |
| Identifier and AuthorityURL | CI_Citation.identifier | The value of 19128:Identifier is equivalent to 19115:CI_Citation.identifier.code. 19128:AuthorityURL contains only the URL of the authority for a namespace, and is equivalent to 19115: CI_Citation.identifier.citation.citedResponsibleParty. contactInfo.onlineResource. 19115 allows a fuller description of the namespace authority. | Check WMO core Profile |
| DataURL | MD_metadata.dataSetURI | equivalent | No change |

Table 6 — Layer attributes

| Attribute | Allowed values | Meaning (0 is default value) | Met Ocean Profile |
| --- | --- | --- | --- |
| queryable | 0, false, 1, true | 0, false: layer is not queryable. 1, true: layer is queryable. | ?? |
| cascaded | 0, positive integer | 0: layer has not been retransmitted by a Cascading Map Server. n: layer has been retransmitted n times. | No change |
| Opaque | 0, false, 1, true | 0, false: map data represents vector features that probably do not completely fill space. 1, true: map data are mostly or completely opaque. | No change |
| noSubsets | 0, false, 1, true | 0, false: WMS can map a subset of the full bounding box. 1, true: WMS can only map the entire bounding box. | No change |
| fixedWidth | 0, positive integer | 0: WMS can produce map of arbitrary width. nonzero: value is fixed map width that cannot be changed by the WMS. | No change |
| fixedHeight | 0, positive integer | 0: WMS can produce map of arbitrary height. nonzero: value is fixed map height that cannot be changed by the WMS. | No change |

Table 7 — Inheritance of Layer properties

| Element | Number | Inheritance | Met Ocean Profile |
| --- | --- | --- | --- |
| Layer | 0+ | no | No change |
| Name | 0/1 a | no | No change |
| Title | 1 | no | No change |
| Abstract | 0/1 | no | No change |
| KeywordList | 0/1 | no | No change |
| Style | 0+ | add | No change |
| CRS | 1+ b | add | No change |
| EX_GeographicBoundingBox | 1 b | replace | No change |
| BoundingBox | 1+ b | replace | No change |
| Dimension | 0+ | replace | No change |
| Attribution | 0/1 | replace | No change |
| AuthorityURL | 0+ | add | No change |
| Identifier | 0+ | no | No change |
| MetadataURL | 0+ | no | No change |
| DataURL | 0/1 | no | No change |
| FeatureListURL | 0/1 | no | No change |
| MinScaleDenominator, MaxScaleDenominator | 0/1 | replace | No change |
| Attributes listed in Table 6 | 0/1 | replace | No change |

a See 7.2.4.6.3 regarding distinction between named and unnamed layers.

b May be 0 only if a value is inherited from an enclosing Layer element; see 7.2.4.6.6 through 7.2.4.6.8

Table 8 — The Parameters of a GetMap request

| Request parameter | Mandatory / Optional | Description | Met Ocean Profile |
| --- | --- | --- | --- |
| VERSION=1.3.0 | M | Request version. | No change |
| REQUEST=GetMap | M | Request name. | No change |
| LAYERS=layer_list | M | Comma-separated list of one or more map layers. | No change |
| STYLES=style_list | M | Comma-separated list of one rendering style per requested layer. | No change |
| CRS=namespace:identifier | M | Coordinate reference system. | No change |
| BBOX=minx,miny,maxx,maxy | M | Bounding box corners (lower left, upper right) in CRS units. | No change |
| WIDTH=output_width | M | Width in pixels of map picture. | No change |
| HEIGHT=output_height | M | Height in pixels of map picture. | No change |
| FORMAT=output_format | M | Output format of map. | No change |
| TRANSPARENT=TRUE¦FALSE | O | Background transparency of map (default=FALSE). | ?? |
| BGCOLOR=color_value | O | Hexadecimal red-green-blue colour value for the background color (default=0xFFFFFF). | ?? |
| EXCEPTIONS=exception_format | O | The format in which exceptions are to be reported by the WMS (default=XML). | No change |
| TIME=time | O | Time value of layer desired. | ?? |
| ELEVATION=elevation | O | Elevation of layer desired. | ?? |
| Other sample dimension(s) | O | Value of other dimensions as appropriate. | ?? Add more detail e.g. 2nd time probability threshold |

Table 9 — The Parameters of a GetFeatureInfo Request

| Request parameter | Mandatory / Optional | Description | Met Ocean Profile |
| --- | --- | --- | --- |
| VERSION=1.3.0 | M | Request version. | No change |
| REQUEST=GetFeatureInfo | M | Request name. | No change |
| map request part | M | Partial copy of the Map request parameters that generated the map for which information is desired. | No change |
| QUERY_LAYERS=layer_list | M | Comma-separated list of one or more layers to be queried. | No change |
| INFO_FORMAT=output_format | M | Return format of feature information (MIME type). | ?? XML+Schema? |
| FEATURE_COUNT=number | O | Number of features about which to return information (default=1). | No change |
| I=pixel_column | M | i coordinate in pixels of feature in Map CS. | No change |
| J=pixel_row | M | j coordinate in pixels of feature in Map CS. | No change |
| EXCEPTIONS=exception_format | O | The format in which exceptions are to be reported by the WMS (default= XML). | ?? |

B.2 Map CS (CRS:1)

Table B.1 — Definition of map coordinate system

| Element name | Entry | Comment | Met Ocean Profile |
| --- | --- | --- | --- |
| Coordinate system identifier | CRS:1 | See 6.7.2 |  |
| Coordinate system type | Cartesian |  |  |
| Datum identifier | computer display |  |  |
| Datum type | engineering |  |  |
| Coordinate system dimension | 2 |  |  |
| Coordinate system axis name | i |  |  |
| Coordinate system axis direction | east | Some maps, especially over the poles, may not have a well-defined linear axis direction. |  |
| Coordinate system axis unit identifier | pixel |  |  |
| Coordinate system axis name | j |  |  |
| Coordinate system axis direction | south | Some maps, especially over the poles, may not have a well-defined linear axis direction. |  |
| Coordinate system axis unit identifier | pixel |  |  |
| Coordinate system remarks | Origin is in upper left. Axis values are non-negative integers. |  |  |

B.3 Layer CRS using WGS 84 longitude-latitude (CRS:84)

Table B.2 — Definition of Layer CRS using WGS 84 longitude-latitude

| Element name | Entry | Comment | Met Ocean Profile |
| --- | --- | --- | --- |
| Coordinate reference system kind code | 1 | Single (not compound) CRS |  |
| Coordinate reference system identifier | CRS:84 |  |  |
| Coordinate reference system valid area | world |  |  |
| Datum identifier | WGS 84 |  |  |
| Datum type | geodetic |  |  |
| Prime meridian identifier | Greenwich |  |  |
| Prime meridian Greenwich longitude | 0 degree |  |  |
| Ellipsoid identifier | WGS 84 |  |  |
| Ellipsoid semi-major axis | 6378137.0 m |  | ?? Cross check |
| Ellipsoid shape | true |  |  |
| Ellipsoid inverse flattening | 298.257223563 |  | ??Cross check |
| Coordinate system identifier | Geodetic Coordinate System |  |  |
| Coordinate system type | geodetic |  |  |
| Coordinate system dimension | 2 |  |  |
| Coordinate system axis name | longitude | The first (x) axis is longitude in this CRS. |  |
| Coordinate system axis direction | east |  |  |
| Coordinate system axis unit identifier | degree |  |  |
| Coordinate axis minimum value | −180 degrees |  |  |
| Coordinate axis maximum value | 180 degrees |  |  |
| Coordinate system axis name | latitude | The second (y) axis is latitude in this CRS. |  |
| Coordinate system axis direction | north |  |  |
| Coordinate system axis unit identifier | degree |  |  |
| Coordinate axis minimum value | −90 degrees |  |  |
| Coordinate axis maximum value | 90 degrees |  |  |

NOTE CRS:84 is permitted to be used at large scales (>10m/pixel) for describing or requesting map layers in any lon/lat

CRS that is equivalent to within ~1m.

Add something like B.6

Table C.1 — Contents of a dimension element

| Field | Mandatory / Optional | Meaning | Met Ocean Profile |
| --- | --- | --- | --- |
| name | M | Attribute stating name of dimensional axis. | No change |
| Units | M | Attribute indicating units of dimensional axis. | No change |
| unitSymbol | O | Attribute specifying symbol. |  |
| Default | O | Attribute indicating default value that will be used if GetMap request does not specify a value. If attribute is absent, then shall respond with a service exception if request does not include a value for that dimension. | M? |
| multipleValues | O | Boolean attribute indicating whether multiple values of the dimension may be requested. 0 (or “false”) = single values only; 1 (or “true”) = multiple values permitted. Default = 0. |  |
| nearestValue | O | Boolean attribute indicating whether nearest value of the dimension will be returned in response to a request for a nearby value. 0 (or “false”) = request value(s) must correspond exactly to declared extent value(s); 1 (or “true”) = request values may be approximate. Default = 0. |  |
| current | O | Boolean attribute valid only for temporal extents (i.e. if attribute name="time"). This attribute, if it either 1 or “true”, indicates (a) that temporal data are normally kept current and (b) that the request parameter TIME may include the keyword “current” instead of an ending value (see C.4.1). Default = 0. | M? |
| Extent | M | Text content indicating available value(s) for dimension. | No change |

# Footnotes

WMO Defines normals as “period averages computed for a uniform and relatively long period comprising at least three consecutive 10 year periods.

# Comments

Do we have any of this?

What should we say about defaults and  nearestValue?

Not sure what to do with this.

This graphic may benefit from clean up.  It is confusing as to what relates to server behavior and what relates to client requests.

There were many comments that the HTTP response header would be hard to implement in clients.

This graphic may benefit from clean up.  It is confusing as to what is mandatory and not for the server and for the client.

How to specify an interval syntactically.

Probably a MUST since 7.2.3 is already a SHALL directive

Probably a MUST since 7.2.3 is already a SHALL directive

MAY would be appropriate because the behavior is truly optional

mBar are only numerically equal to hPa on Earth. Meteorologists use hPa.