# INSPIRE TWG AC-MF Use Case 1

# – Use of Meteorology in Support of Emergency Response

# – Sub-case: Plume Prediction

Draft Version 0.3 (20 August 2010)

## Description

The Met Office is the official source of weather information in the UK. It provides a number of services to help authorities prepare for, and respond to, emergencies [1]. The weather can be the cause of an emergency and/or have a major influence on its impact. Legislation supporting the UK Civil Contingencies Act 2004 [2] states that Category 1 Responders must have regard to the Met Office’s duty to warn the public and provide information and advice, if an emergency is likely to occur or has taken place.

Met Office forecasters, specialist scientists and advisors provide expert advice on the interpretation and impact of the weather during an emergency. Public Weather Service (PWS) Advisors from the Met Office also assist in the development and maintenance of risk registers, input to exercise and planning processes and attend incident command and control centres. The Environment Monitoring and Response Centre (EMARC), a forecast production unit at the Met Office, provides specialist meteorological information to deal with a variety of   environmental incidents (and for exercises) to the UK emergency services and other government departments, as well as to the international community and operates 24 hours a day, 365 days a year.

The Met Office can provide plume predictions during emergencies, which sees EMARC forecasters interpreting data from the latest observations as well as from sophisticated computer models to deduce the local weather conditions and the areas at risk from the pollutant. Local variations in wind speed and direction are the main influencers on dispersion. Rain at the scene or downwind can also wash the pollutant out of the atmosphere leading to higher concentrations on the ground. The vertical temperature profile of the atmosphere also affects the stability of the air and this determines how high the plume is likely to rise, which subsequently affects the distance it might travel and its behaviour close to hills. This service covers a range of incident types can result in the release of a potentially hazardous plume:

Fire (e.g. fire at a chemical plant or oil refinery);

Chemical Release (e.g. chemical spillage or a road traffic accident in which a hazardous substance has either escaped or ignited);

Biological Incidents (e.g. foot & mouth, blue tongue)

Nuclear Release (e.g. accident at nuclear power plant);

Volcanic Eruption (i.e. prediction of ash plume).

EMARC uses NAME (Numerical Atmospheric dispersion Modelling Environment), which utilises a Lagrangian approach to determine the location of a plume: pollutants are represented by a large number of model ‘particles’ which are released into the modelled atmosphere at the source location. These particles are affected by the local wind speed, atmospheric turbulence, precipitation, and other processes. Each model ‘particle’ can have its own characteristics, represent different compounds, chemicals and real particulate sizes, and can be affected by temporal and spatial variations in the meteorology including turbulence and loss processes such as precipitation. This enables NAME to simulate highly complex dispersion events, to predict the movement of a wide range of pollutants in the atmosphere.

Although these ‘model particles’ can be shown output directly, either as plots showing each particle at a given time (possibly with colouring used to show height) or as particle trajectories, they are usually accumulated into three-dimensional cells on a regular grid, to give concentration (potentially at different vertical levels and times). They may alternatively be shown in terms of standard deviation from the mid-plume value at a given radius from the release site, a so-called “Area at Risk Map” (usually with at least two threshold values); this is important for early predictions, where the details of release concentrations can be limited, and a prediction of a actual concentration could be misleading.

On notification of an incident, EMARC forecasters will run NAME, having input all information provided about the release, to predict the movement, deposition and dispersal of large plumes of material for periods of time ranging from hours to several days. The model produces a geographical display of the movement of the plume showing the area at risk. The response time for providing this information varies from 20 minutes for small scale events to approximately one hour for a full 5-day prediction. The NAME model can be re-run as more detail becomes available following an accident, providing more precise concentration and deposition values. However, in many incidents it is often hours into an event before the composition of chemicals or substances involved is fully known.

EMARC use a number of standard screens to configure the input to the NAME model for different cases, but the model is highly configurable, and for more involved situations or non-standard cases, the Met Office Atmospheric Dispersion Group (ADG) will become involved in the process of running the model. Unlike NWP models, the output is not usually a ‘complete set’, but only those parameters, heights, times, etc that are of interest (and for efficiency, zero values are not output).

The services provided range from an immediate prediction of the direction of the plume, to allow safe approach to an incident (FireMet), through to short-range predictions of areas of risk (e.g. CHEMET (chemical), PACRAM (nuclear)) and longer-range prediction of areas at risk (e.g. Volcanic Ash Advisory) and the identification of the likely origin of particular pollutant (e.g. use of RIMNET radiation monitoring with NAME for nuclear incidents). The figures below show examples of the products generated.

a) NAME model forecast pollutant concentrations

b) FireMet Wind & Hazard Sector and Precipitation, Temperature & Humidity time series in graphical and tabular form

c) CHEMET Area At Risk Map for two threshold values of standard deviation from the concentration at the centre of the plume for a given radial distance from the release site

d) Volcanic Ash Advisory for a flight level range, showing three levels of concentration

e) Volcanic Ash Advisory showing boundary polygons for single concentration threshold at three flight levels for four different times, drawn by a Forecaster, based on NAME output

f) Source of plume shown as probabilities

## High Level Use Case

The Use Case diagram below shows all the use cases and actors considered. Use cases are colour-coded to indicate their focus, with blue writing used to show the ‘super use case’ for plume prediction and red writing used to show the four main more specific use cases, which are described in the following section; all other use case area not explicitly detailed, but may appear as a step within the main use cases. Large actors are involved in the detailed use cases; small actors are included to provide a wider context, but are not involved directly in the detailed use cases.

### Actors

Emergency Responder – organisations heavily involved in managing incident (exactly which organisations will depend on the nature of the incident)

Category 1 Responders – e.g. emergency services, local authorities, NHS bodies; see Annex A

Category 2 Responders – e.g. Health and Safety Executive, transport and utility companies; see Annex A

Monitoring Site – site measuring a particular pollutant

Strategic Command – a general class of actor used to describe the range of groups which may come together to carry out a strategic role in the management of an incident

Bronze Command – operation command at incident site (police or fire officer)

Silver Command – tactical command within site of incident (usually senior police office)

Gold Command – strategic command and control centre remote from incident (chief police constable)

Cabinet Office Briefing Room (COBR) – central government crisis response committee (usually chaired by Prime Minister)

Scientific & Technical Advice Cell (STAC) – established to coordinate multi-agency specialist advice to Gold Command

General Public (i.e. citizens)

Public Weather Service (PWS) Advisors (i.e. forecast advisors)

Met Office Plume Prediction Expert – a general class of actor used to describe the Met Office experts involved in providing plume prediction services

Environment Monitoring and Response Centre (EMARC) –  specialist forecast production unit at the Met Office

Atmospheric Dispersion Group (ADG) – Met Office team responsible for developing NAME, who provide operational input in more specialist situations

Realtime Observations Database (MetDB) – source of real-time observations at the Met Office

Numerical Weather Prediction (NWP) Capability – range of NWP models and post-processing, which provides automated weather forecasts (especially 25 km Global and 12 km North Atlantic & Europe models)

UK (NWP) Post-Processing (UKPP) Capability – applications employing down-scaling and rapid updates (nowcasts) to provide a high-resolution (2 km) weather forecasts for the UK

Numerical Atmospheric dispersion Modelling Environment (NAME) - Lagrangian model used to determine the location of a plume

Digital Map Management System (DMMS) – Database of map overlays at wide range of scales.

## Detailed Structured Description of Plume Prediction Use Cases

The plume prediction use cases are presented in more detail using a standard template in the following sections, with primary example (and other examples) indicated in brackets in the title.

### Use Case 1: Identify Safe Approach to Incident

| Use Case 1 | Identify safe approach to incident (FireMet) |
| --- | --- |
| Priority | High |
| Description | Provide Fire and Rescue Service (FRS) responders with the latest weather information to help them identify a safe approach when dealing with a major incident. Provides immediate access to forecast conditions, before a more detailed area at risk product is available. This is realised through a fully automated, password-protected, web-based system available to all FRS Incident Command Units, mobilising centres and the National Coordination Centre. |
| Pre-condition | An incident releasing a plume has occurred. |
| Flow of Events - Basic Path |
| Step 1 | Emergency Responders provide the Incident Location via webpage |
| Step 2 | FireMet Application automatically obtains Current Weather data by interpolating from the High-Resolution Post-Processed Model Analysis/Forecast provided by UK (NWP) Post-Processing (UKPP) Capability |
| Step 3 | FireMet Application automatically generates Hazard Sector visualisation, with supporting text, and a presentational form of Current Weather (table & graph) on the webpage |
| Step 4 | Emergency Responders review the Hazard Sector and Current Weather products on a Webpage |
| Post-condition | Emergency responders understand the safe approach directions to the incident. |
| Data Source: Incident Location |
| Description | Location of incident as: Place name or Postcode (e.g. EX1 3PB) Country map grid reference (e.g. GB Ordnance Survey: SX500534) or grid coordinates (e.g. UK eastings, northings: 377400, 399500) Latitude & Longitude |
| Data Provider | Fire and Rescue Service (FRS) responders |
| Geographic Scope | Point (or Polygon as proxy for point) within UK |
| Thematic Scope | Addresses (AD), Coordinate Reference Systems (RS) |
| Scale, resolution | Point or Polygon |
| Delivery | Webpage entry |
| Documentation | None |
| Data Source: Current Weather |
| Description | Point interpolation from high-resolution post-processed model analysis / forecast provided as: Table (text) of Temperature, Humidity, Precipitation Type, Precipitation rate, Hazard Sector, wind speed Wind direction; Graphs of Precipitation rate, Temperature and Humidity against time. Example shown in figure (b) |
| Data Provider | Met Office |
| Geographic Scope | Point within UK |
| Thematic Scope | Atmospheric Conditions (AC), Meteorological Geographic Features (MF) |
| Scale, resolution | PointSeries (hourly data for 6-hour window centred on current hour) |
| Delivery | Webpage |
| Documentation | http://www.metoffice.gov.uk/corporate/pws/emergency_response.pdf (section 3.8 FireMet) |
| Supporting Data Source: High-Resolution Post-Processed Model Analysis/Forecast |
| Description | High-resolution NWP model analyses and forecasts post-processed to produce gridded data accounting for local topographic effects. |
| Data Provider | Met Office |
| Geographic Scope | UK |
| Thematic Scope | Atmospheric Conditions (AC), Meteorological Geographic Features (MF) |
| Scale, resolution | GridSeries (1.5 km resolution; hourly, past times as analyses, forecasts out to 36 hours) |
| Delivery | Standard output is in a Met Office bespoke Nimrod format, which is also converted to GRIB. |
| Documentation | http://www.metoffice.gov.uk/research/areas/numerical-modelling/post-processing http://www.metoffice.gov.uk/science/creating/daysahead/nwp/um_config.html |
| Data Source: Hazard Sector |
| Description | Point interpolation from high-resolution post-processed model analysis provided as: Visualisation of ‘Hazard Sector’, with wind speed and direction Table with text information on Hazard Sector and wind (in range of formats) Example shown in figure (b) |
| Data Provider | Met Office |
| Geographic Scope | Point within UK |
| Thematic Scope | Atmospheric Conditions (AC), Meteorological Geographic Features (MF) |
| Scale, resolution | Point; TimeInstant (current hour) |
| Delivery | Webpage |
| Documentation | http://www.metoffice.gov.uk/corporate/pws/emergency_response.pdf (section 3.8 FireMet) |

### Use Case 2: Identify area at risk from plume

| Use Case 2 | Identify areas at risk from plume (CHEMET, PACRAM) |
| --- | --- |
| Priority | High |
| Description | Identify the areas at risk from the plume and the local weather conditions for the next few hours in the form of a snapshot. |
| Pre-condition | An incident releasing a plume has occurred. |
| Flow of Events - Basic Path |
| Step 1 | Emergency Responders provides Incident Details by phone, which is recorded using a CHEMET Form A. |
| Step 2 | Environment Monitoring and Response Centre (EMARC) use the Incident Details to initialise the Numerical Atmospheric-dispersion Modelling Environment (NAME) |
| Step 3 | NAME runs to generate a NAME Forecast ,using either: Model Analyses/Forecasts generated by the Numerical Weather Prediction (NWP) Capability; or: Weather Observation provided by Meteorological (observations) Database (MetDB). |
| Step 4 | NAME generates an Area At Risk Map using a Map Overlay obtained from the Digital Map Management System (DMMS) |
| Step 5 | EMARC generates Forecast of Relevant Meteorological Parameters, using either the Model Analyses/Forecasts or Weather Observations. |
| Step 6 | EMARC delivers Area At Risk Map and Forecast of Relevant Meteorological Parameters to the Emergency Responders in the form of a CHEMET Form B by website, email or fax |
| Post-condition | Emergency responders have received and understood briefing material. |
| Data Source: Plume Incident Details |
| Description | Details including: National Grid coordinates (eastings, northings) and address of the incident location Time of the event Any additional information on the chemicals involved Site characteristics (Urban, Rural, Coastal) Nature of Release (Continuous , Instantaneous, Fire at site) If available, details of the current weather at the site |
| Data Provider | Emergency Services |
| Geographic Scope | Point within UK |
| Thematic Scope | Addresses (AD), Coordinate Reference Systems (RS), Atmospheric Conditions (AC), Meteorological Geographic Features (MF) |
| Scale, resolution | Point; TimeInstant |
| Delivery | Phone to populate CHEMET Form A |
| Documentation | http://www.metoffice.gov.uk/publicsector/CHEMET/ |
| Data Source: Numerical Atmospheric Modelling Environment (NAME) Forecast |
| Description | 4-dimensional (3d space & time) predictions of pollutant concentration. The concentrations of the tracked parcels of air are mapped onto regular grid-boxes. Note that only the required data are output, resulting, resulting in limited sets of variables & levels, and ‘sparse’ grids (values only held where non-zero) |
| Data Provider | Met Office |
| Geographic Scope | Area of interest within UK |
| Thematic Scope | Atmospheric Conditions (AC), Meteorological Geographic Features (MF) |
| Scale, resolution | GridSeries (spatial and temporal resolution depends on area of interest) |
| Delivery | Standard output is in a text form, which is converted to netCDF (and GRIB2) for visualisation in a GIS environment. |
| Documentation | http://www.metoffice.gov.uk/environment/name.html |
| Data Source: Model Analysis/Forecast |
| Description | A range of NWP models provide automated weather forecasts (especially 25 km Global and 12 km North Atlantic & Europe models) as 4-dimensional (3d space & time) fields. |
| Data Provider | Met Office |
| Geographic Scope | UK |
| Thematic Scope | Atmospheric Conditions (AC), Meteorological Geographic Features (MF) |
| Scale, resolution | GridSeries (1.5 km resolution; hourly, past times as analyses, forecasts out to 36 hours) |
| Delivery | Standard output is in a Met Office bespoke FieldsFile format, which is also converted to GRIB. |
| Documentation | http://www.metoffice.gov.uk/research/areas/numerical-modelling/post-processing http://www.metoffice.gov.uk/science/creating/daysahead/nwp/um_config.html |
| Data Source: Weather Observations |
| Description | Observations of the weather from a nearby observing site, in WMO BUFR format. |
| Data Provider | Met Office |
| Geographic Scope | Point within UK, but representative of local area of interest |
| Thematic Scope | Atmospheric Conditions (AC), Meteorological Geographic Features (MF) |
| Scale, resolution | Point or PointSeries |
| Delivery | n/a |
| Documentation | None |
| Data Source: Map Overlay |
| Description | High-resolution geographical map |
| Data Provider | Ordnance Survey |
| Geographic Scope | Area of interest within UK |
| Thematic Scope | Cadastral Parcels (CP)? |
| Scale, resolution | Polygons provided as raster image (1:50,000) |
| Delivery | Website, email or fax (as part of Area at Risk Map product) |
| Documentation | None |
| Data Source: Area At Risk Map |
| Description | Product generated by NAME showing the prediction of the plume extent, for two threshold values of standard deviation from the concentration at the centre of the plume for a given radial distance from the release site. This is visualised in combination with a UK (Ordnance Survey) Map Overlay. Example shown in figure (c) |
| Data Provider | Met Office |
| Geographic Scope | Area of interest within UK |
| Thematic Scope | Atmospheric Conditions (AC), Meteorological Geographic Features (MF) |
| Scale, resolution | Grid; TimePeriod (representing area of interest; typically 3-4 hour validity period (but left to the forecaster’s discretion), with updates as necessary 30 minutes before existing forecast expires) |
| Delivery | Website, email or fax (CHEMET Form B) |
| Documentation | http://www.metoffice.gov.uk/publicsector/CHEMET/ |
| Data Source: Forecast of Relevant Meteorological Parameters |
| Description | Product generated Model Analyses/Forecasts covers: Surface wind direction (8-point compass degrees true) Wind speed at 10 metres above ground level (kilometres per hour.) Indication of the behaviour of the plume due to weather conditions while the chemical is assumed to have neutral buoyancy Total cloud cover (oktas), with height (in feet above ground level) of the lowest significant cloud layer (5 oktas or more) Temperature Relative humidity. Intensity & type of precipitation Depth of the mixing layer Mean wind in the mixing layer Estimate of the vertical stability of the atmosphere using the Pasquill Stability Index Any changes during the period are given remarks sections. |
| Data Provider | Met Office |
| Geographic Scope | Point within UK, but representative of local area of interest |
| Thematic Scope | Atmospheric Conditions (AC), Meteorological Geographic Features (MF) |
| Scale, resolution | Point or Polygon; TimePeriod (representing area of interest; typically 3-4 hour validity period (but left to the forecaster’s discretion), with updates as necessary 30 minutes before existing forecast expires) |
| Delivery | Website, email or fax (CHEMET Form B) |
| Documentation | http://www.metoffice.gov.uk/publicsector/CHEMET/ |

### Use Case 3: Predict pollutant concentrations & deposition

| Use Case 3 | Predict pollutant concentrations & deposition (Volcanic Ash, CHEMETPro, RSMC,RIMNET, Animal Health) |
| --- | --- |
| Priority | High |
| Description | Provide predictions of the pollutant concentrations and deposition of the pollutant from the plume incident out from a few hours to a week ahead in the form of an animation (or series of snapshots). N.B. Only pollutant concentration product is described below, but similar products can be generated for deposition. |
| Pre-condition | Either incident is already being monitored, or large-scale incident is detected or notified (e.g. volcanic eruption). |
| Flow of Events - Basic Path |
| Step 1 | Monitoring Site (e.g. Volcanic Ash Advisory Centre) (or possibly Emergency Responders) provide Incident Details. |
| Step 2 | Environment Monitoring and Response Centre (EMARC) use the Incident Details to initialise the Numerical Atmospheric-dispersion Modelling Environment (NAME) (including selection from drop-down menus, to specify incident area, plume height, chemical species or particle size distribution, etc). |
| Step 3 | NAME runs to generate a NAME Forecast using from the Model Analyses/Forecasts provided from the Numerical Weather Prediction (NWP) Capability. |
| Step 4 | NAME generates Pollutant Concentrations Forecast using a Map Overlay obtained from the Digital Map Management System (DMMS) |
| Step 5 | EMARC delivers Pollutant Concentrations Forecast to the Emergency Responders (and possibly the General Public) by either WMO GTS, website, email or fax |
| Post-condition | Emergency responders (and General Public) have received and understood briefing material. |
| Flow of Events - Alternative Path 1 |
| Replace Step 2 | Atmospheric Dispersion Group (ADG) carries out more complex configuration and initialisation of NAME using the Incident Details. |
| Flow of Events - Alternative Path 2 |
| Additional Step 4a | Environment Monitoring and Response Centre (EMARC) draws simpler polygons around the Pollutant Concentration Forecast to generate a variant of this product. |
| Data Source: Plume Incident Details |
| Description | Details including: Location Time of the event As much information on the plume characteristics as possible |
| Data Provider | Volcanic Ash Advisory Centres (with initial identification by eye witnesses or volcanic eruption detection system) |
| Geographic Scope | Point, potentially anywhere on the globe |
| Thematic Scope | Coordinate Reference Systems (RS) |
| Scale, resolution | Point |
| Delivery | Phone |
| Documentation | http://www.metoffice.gov.uk/aviation/vaac/eruption_detection.html |
| Data Source: Numerical Atmospheric Modelling Environment (NAME) Forecast |
| Description | 4-dimensional (3d space & time) predictions of pollutant concentration. The concentrations of the tracked parcels of air are mapped onto regular grid-boxes. Note that only the required data are output, resulting, resulting in limited sets of variables & levels, and ‘sparse’ grids (values only held where non-zero) |
| Data Provider | Met Office |
| Geographic Scope | Area of interest within UK |
| Thematic Scope | Atmospheric Conditions (AC), Meteorological Geographic Features (MF) |
| Scale, resolution | GridSeries (spatial and temporal resolution depends on area of interest) |
| Delivery | Standard output is in a text form, which is converted to netCDF (and GRIB2) for visualisation in a GIS environment. |
| Documentation | http://www.metoffice.gov.uk/environment/name.html |
| Data Source: Model Analysis/Forecast |
| Description | A range of NWP models provide automated weather forecasts (especially 25 km Global and 12 km North Atlantic & Europe models) as 4-dimensional (3d space & time) fields. |
| Data Provider | Met Office |
| Geographic Scope | UK |
| Thematic Scope | Atmospheric Conditions (AC), Meteorological Geographic Features (MF) |
| Scale, resolution | GridSeries (1.5 km resolution; hourly, past times as analyses, forecasts out to 36 hours) |
| Delivery | Standard output is in a Met Office bespoke FieldsFile format, which is also converted to GRIB. |
| Documentation | http://www.metoffice.gov.uk/research/areas/numerical-modelling/post-processing http://www.metoffice.gov.uk/science/creating/daysahead/nwp/um_config.html |
| Data Source: Map |
| Description | Geographical map at appropriate scale |
| Data Provider | Various |
| Geographic Scope | Area of interest, potentially anywhere on the globe |
| Thematic Scope | Cadastral Parcels (CP)? |
| Scale, resolution | Polygons provided as raster image |
| Delivery | Website, email or fax (as part of Pollutant Concentrations Forecast product) |
| Documentation | None |
| Data Source: Pollutant Concentrations Forecast |
| Description | Generated product from NAME Forecast shows sequence of charts showing the predicted evolution of the plume extent at different heights and different times for multiple thresholds. These are shown as raster, filled contour or polygons (which also may be colour-filled); the polygons are also produced as a text product. This is visualised in combination with an appropriate Map Overlay. Examples of the three forms shown in figure (a), (d) and (e) respectively. |
| Data Provider | Met Office |
| Geographic Scope | Area of interest, potentially anywhere on the globe |
| Thematic Scope | Atmospheric Conditions (AC), Meteorological Geographic Features (MF) |
| Scale, resolution | GridSeries or PolygonSeries (representing area of interest which may extend outside the UK, and time scales of interest out to 5 days or more) |
| Delivery | (WMO) Global Telecommunications System (GTS), website, email or fax |
| Documentation | http://www.metoffice.gov.uk/aviation/vaac/forecasting.html |

### Use Case 4: Identify source of pollutant

| Use Case 4 | Identify Source of Pollutant (Radiological Incident Detection) |
| --- | --- |
| Priority | High |
| Description | Identify the likely area of origin in of a particular measured pollutant as area-based probability |
| Pre-condition | A particular pollutant has been detected at one or more monitoring sites. |
| Flow of Events - Basic Path |
| Step 1 | Monitoring Site provides Pollutant Observations data. |
| Step 2 | Environment Monitoring and Response Centre (EMARC) or the Atmospheric Dispersion Group (ADG) uses the Pollutant Observations to initialise the Numerical Atmospheric-dispersion Modelling Environment (NAME). |
| Step 3 | NAME runs ‘backwards’ to generate a NAME Forecast using from the Model Analyses/Forecasts provided from the Numerical Weather Prediction (NWP) Capability. |
| Step 4 | NAME generates Plume Origin Prediction from NAME forecast using a Map Overlay obtained from the Digital Map Management System (DMMS) |
| Step 5 | EMARC delivers Plume Origin Prediction to the Emergency Responders by either website, email or fax |
| Post-condition | Emergency responders have received and understood briefing material. |
| Data Source: Polluant Observations |
| Description | Measurement of a particular pollutant by a sensor at a particular site. Detection of the pollutant at multiple sites would usually be required. |
| Data Provider | Various monitoring organisations (depending on pollutant type) |
| Geographic Scope | Single point usually within UK |
| Thematic Scope | Environmental Monitoring Facilities (EF) |
| Scale, resolution | PointSeries (a number of points, with time period depending on what is available) |
| Delivery | Various |
| Documentation | None |
| Data Source: Numerical Atmospheric Modelling Environment (NAME) Forecast |
| Description | 4-dimensional (3d space & time) predictions of pollutant concentration. The concentrations of the tracked parcels of air are mapped onto regular grid-boxes. Note that only the required data are output, resulting, resulting in limited sets of variables & levels, and ‘sparse’ grids (values only held where non-zero). |
| Data Provider | Met Office |
| Geographic Scope | Area of interest within UK |
| Thematic Scope | Atmospheric Conditions (AC), Meteorological Geographic Features (MF) |
| Scale, resolution | GridSeries (spatial and temporal resolution depends on area of interest) |
| Delivery | Standard output is in a text form, which is converted to netCDF (and GRIB2) for visualisation in a GIS environment. |
| Documentation | http://www.metoffice.gov.uk/environment/name.html |
| Data Source: Model Analysis/Forecast |
| Description | A range of NWP models provide automated weather forecasts (especially 25 km Global and 12 km North Atlantic & Europe models) as 4-dimensional (3d space & time) fields. |
| Data Provider | Met Office |
| Geographic Scope | UK |
| Thematic Scope | Atmospheric Conditions (AC), Meteorological Geographic Features (MF) |
| Scale, resolution | GridSeries (1.5 km resolution; hourly, past times as analyses, forecasts out to 36 hours) |
| Delivery | Standard output is in a Met Office bespoke FieldsFile format, which is also converted to GRIB. |
| Documentation | http://www.metoffice.gov.uk/research/areas/numerical-modelling/post-processing http://www.metoffice.gov.uk/science/creating/daysahead/nwp/um_config.html |
| Data Source: Map |
| Description | Geographical map at appropriate scale |
| Data Provider | Various |
| Geographic Scope | Area of interest, potentially anywhere on the globe |
| Thematic Scope | Cadastral Parcels (CP)? |
| Scale, resolution | Polygons provided as raster image |
| Delivery | Website, email or fax (as part of Plume Origin Prediction product) |
| Documentation | None |
| Data Source: Plume Origin Prediction |
| Description | Generated product from the NAME Forecast, shows the likelihood of a plume originating from within the area of the cell of a raster map, as a probability (most cells will have a zero probability). This is visualised in combination with an appropriate Map Overlay. Example shown in figure (f) |
| Data Provider | Met Office |
| Geographic Scope | Area of interest, potentially anywhere on the globe |
| Thematic Scope | Atmospheric Conditions (AC), Meteorological Geographic Features (MF) |
| Scale, resolution | Variable, depending on area of interest |
| Delivery | Webpage, email or fax |
| Documentation | http://www.metoffice.gov.uk/corporate/pws/emergency_response.pdf (section 3.6 Source Identification) |

# References

The Met Office’s role in emergency preparedness and response: http://www.metoffice.gov.uk/corporate/pws/emergency_response.pdf

UK Civil Contingencies Act (Cabinet Office): http://www.cabinetoffice.gov.uk/ukresilience/preparedness/ccact.aspx

# Annex 1:  Category 1 & 2 Responders

## Category 1 Responders

Those organisations at the core of the response to most emergencies (e.g. emergency services, local authorities, NHS bodies). Category 1 responders are subject to the full set of civil protection duties. They will be required to:

Assess the risk of emergencies occurring and use this to inform contingency planning;

Put in place emergency plans;

Put in place Business Continuity Management arrangements;

Put in place arrangements to make information available to the public about civil protection matters and maintain arrangements to warn, inform and advise the public in the event of an emergency;

Share information with other local responders to enhance co-ordination;

Co-operate with other local responders to enhance co-ordination and efficiency; and * Provide advice and assistance to businesses and voluntary organisations about business continuity management (Local Authorities only).

Category 2 Responders

These "co-operating bodies" (e.g. Health and Safety Executive, transport and utility companies) are less likely to be involved in the heart of planning work but will be heavily involved in incidents that affect their sector. Category 2 responders have a lesser set of duties - co-operating and sharing relevant information with other Category 1 and 2 responders.

# Footnotes

Category 1 responders are those organisations at the core of the response to most emergencies (e.g. emergency services, local authorities, NHS bodies).